## Slide 1: Computer Architectures Session 2
RISC-V Processor Pipelining
TAs :
  Xiaoling Yi (xiaoling.yi@kuleuven.be)
  Chao Fang (chao.fang@kuleuve.be)
  Adrian Kneip (adrian.kneip@kuleuve.be)

## Slide 2: Timeline
Session 1
Session 2
Session 3
Simulation
Functional single cycle processor
Single cycle processor with multiplication
Pipelined processor
Data hazard resolution
Advanced acceleration
Project Feedback
[Mar-05/06]
[Apr-02/03]
[Apr-23/24]
Session 4
[May-7/8]
Written Exam Exercises
Submission Deadline [May-2]
Backend flow (synthesis-only)
Control hazard resolution
Final Schedule

## Slide 3: Last session recap
Single cycle processor skeleton
Functional single cycle processor
Single cycle processor with multiplication
Pipelined processor
Pipelined processor with data hazard resolution
Advanced acceleration
Simulation
Backend flow (synthesis-only)
Backend flow (basic)
Session 1
Session 2
Session 3
[Mar-05/06]

## Slide 4: Last session recap
Single-cycle Processor
Simple_program
Mult1
Mult2
Prerequisite for this session!

## Slide 5: Today’s session: Pipelined processor
Single cycle processor skeleton
Functional single cycle processor
Single cycle processor with multiplication
Pipelined processor
Pipelined processor with data hazard resolution
Advanced acceleration
Simulation
Backend flow (synthesis-only)
Backend flow (complete)
Session 1
Session 2
Session 3
[Apr-02/03]

## Slide 6: 5-stage Pipelining
Fetch
Decode
Execute
Memory
Write Back
Define pipeline stages
Allocate processor modules
Insert pipeline registers (---)

## Slide 7: 5-stage Pipelining
Pipeline registers

## Slide 8: 5-stage Pipelining
At clock cycle 5:
Inst 1 -> write back
Inst 2 -> data
Inst 3 -> execute
Inst 4 -> decode
Inst 5 -> fetch

## Slide 9: Today’s session: Pipelined processor
Single cycle processor skeleton
Functional single cycle processor
Single cycle processor with multiplication
Pipelined processor
Pipelined processor with data hazard resolution
Advanced acceleration
Simulation
Backend flow (synthesis-only)
Backend flow (complete)
Session 1
Session 2
Session 3
[Apr-02/03]
Obj-1: mult2

## Slide 10: Obj-1: mult2
Pipelined processor
  Introduce the pipeline registers to cpu.v to support pipelined execution
  Run MULT2
  Run backend flow, track the timing and area change along the steps.
    Synthesis -> Floorplan -> Signoff
  Complete the report
MULT2
# load operands
ld x8, 0(x0)
ld x9, 8(x0)
ld x10, 16(x0)
ld x11, 24(x0)
ld x12, 32(x0)
ld x13, 40(x0)
ld x14, 48(x0)
ld x15, 56(x0)
ld x16, 64(x0)
ld x17, 72(x0)
# multiplication
mul x18, x8, x9
mul x19, x10, x11
mul x20, x12, x13
mul x21, x14, x15
mul x22, x16, x17
#sums
addi x23, x0, 0
nop
nop
nop
add x23, x23, x18
nop
nop
nop
add x23, x23, x19
nop
nop
nop
add x23, x23, x20
nop
nop
nop
add x23, x23, x21
nop
nop
nop
add x23, x23, x22
nop
nop
nop
nop
Pipelined processor

## Slide 11: Implementation Method
Stage | IF | ID | EXE | MEM | WB
Data Path resources | instruction_memory | register_file |  |  | 
Pipe. Reg. | IF/ID | ID/EXE | EXE/MEM | MEM/WB
Signals | instruction |  |  | 
EXAMPLE
You can find this helper table in TASKS TO BE DONE of session_guide.pdf

## Slide 12
// IF STAGE wire [ 31:0] instruction, instruction_IF_ID, instruction_MEM_WB;
sram_BW32 #( .ADDR_W(9 ), .DATA_W(32) ) instruction_memory( .clk (clk ), .addr (current_pc ), .wen (1'b0 ), .ren (1'b1 ), .wdata (32'b0 ), .rdata (instruction ), // Wiring component .addr_ext (addr_ext ), // to appropriate stage .wen_ext (wen_ext ), .ren_ext (ren_ext ), .wdata_ext(wdata_ext ), .rdata_ext(rdata_ext ) );
// IF_ID Pipeline register for instruction signal reg_arstn_en#( .DATA_W(32) // width of the forwarded signal )signal_pipe_IF_ID( .clk (clk ), .arst_n (arst_n ), .din (instruction ), .en (enable ), .dout (instruction_IF_ID) )
// ID STAGE
register_file #( .DATA_W(64) ) register_file( .clk (clk ), .arst_n (arst_n ), .reg_write(reg_write ), .raddr_1 (instruction_IF_ID[19:15]), // Wiring component .raddr_2 (instruction_IF_ID[24:20]), // to appropriate stage .waddr (instruction_MEM_WB[11:7] ),// Reg_write addr .wdata (regfile_wdata ), .rdata_1 (regfile_rdata_1 ), .rdata_2 (regfile_rdata_2 ) );
Stage | IF | ID | EXE | MEM | WB
Data Path resources | Instruction_memory | register_file |  |  | 
Pipe. Reg. | IF/ID | ID/EXE | EXE/MEM | MEM/WB
Signals | Instruction_IF_ID |  |  | Instruction_MEM_WB
EXAMPLE
Tips:
Be careful with each register’s DATA_WIDTH.
Always define the signal before usage in coding.
*_ext wires are only for the testbench (do not change).
Coding Example (cpu.v)
The IF_ID Pipeline Register.
Implementation Method
You can find this helper table in TASKS TO BE DONE of session_guide.pdf

## Slide 13: Implementation Method
// IF STAGE wire [ 31:0] instruction, instruction_IF_ID, instruction_MEM_WB;
sram_BW32 #( .ADDR_W(9 ), .DATA_W(32) ) instruction_memory( .clk (clk ), .addr (current_pc ), .wen (1'b0 ), .ren (1'b1 ), .wdata (32'b0 ), .rdata (instruction ), // Wiring component .addr_ext (addr_ext ), // to appropriate stage .wen_ext (wen_ext ), .ren_ext (ren_ext ), .wdata_ext(wdata_ext ), .rdata_ext(rdata_ext ) );
// IF_ID Pipeline register for instruction signal reg_arstn_en#( .DATA_W(32) // width of the forwarded signal )signal_pipe_IF_ID( .clk (clk ), .arst_n (arst_n ), .din (instruction ), .en (enable ), .dout (instruction_IF_ID) )
// ID STAGE
register_file #( .DATA_W(64) ) register_file( .clk (clk ), .arst_n (arst_n ), .reg_write(reg_write ), .raddr_1 (instruction_IF_ID[19:15]), // Wiring component .raddr_2 (instruction_IF_ID[24:20]), // to appropriate stage .waddr (instruction_MEM_WB[11:7] ),// Reg_write addr .wdata (regfile_wdata ), .rdata_1 (regfile_rdata_1 ), .rdata_2 (regfile_rdata_2 ) );
EXAMPLE
Tips:
Be careful with each register’s DATA_WIDTH.
Always put the signal definition before usage.
*_ext wires are only for the cpu_tb.v initialization.
Sample Code Snippet
The IF_ID Pipeline Register.
Stage | IF | ID
Data Path resources | Instruction_memory | register_file
Pipe. Reg. | IF/ID
Signals | Instruction_IF_ID
①
②
①
②
①
②
Refer to the 5-stage pipeline to implement step by step.

## Slide 14: Implementation Method
// cpu.v
reg_arstn_en#( .DATA_W(32) )signal_pipe_IF_ID( .clk (clk ), .arst_n (arst_n ), .din (instruction ), .en (enable ), .dout (instruction_IF_ID) )
EXAMPLE
Module instantiation
1. The Template Definition
// reg_arstn_en.v
module reg_arstn_en#(
parameter integer DATA_W = 20,
parameter integer PRESET_VAL = 0
)(
input clk,
input arst_n,
input en,
input [ DATA_W-1:0] din,
output [ DATA_W-1:0] dout
);
2. The Instance Declaration
Template Name
Instance Name
Port
Name
Signal
Connection
Parameterization
If you need a customized module, you should also follow this approach.

## Slide 15
Stage | IF | ID | EXE | MEM | WB
Data Path resources | IMEM PC | Control Unit Register File … | ALU … | … | …
Pipe. Reg. | IF/ID | ID/EXE | EXE/MEM | MEM/WB
Signals | Instruction_IF_ID | ControlSignals_ID_EX RegFile_data_1_ID_EX … | … | …
EXAMPLE
Sample Code Snippet
What should the final table be like?
Use it as a checklist to save the debugging time!
// IF STAGE BEGIN
... // IF STAGE END
// IF_ID REG BEGIN
... // IF_ID REG END
// ID STAGE BEGIN
... // ID STAGE END
// ID_EX REG BEGIN
... // ID_EX REG END
// EX STAGE BEGIN
... // EX STAGE END
// EX_MEM REG BEGIN
... // EX_MEM REG END
// MEM STAGE BEGIN
... // MEM STAGE END
// MEM_WB REG BEGIN
... // MEM_WB REG END
// WB STAGE BEGIN
... // WB STAGE END
Linting your code.
These should be the wire names (instances) you choose in your design.
Implementation Method

## Slide 16: Today’s session: Pipelined processor w/ hazard
Single cycle processor skeleton
Functional single cycle processor
Single cycle processor with multiplication
Pipelined processor
Pipelined processor with data hazard resolution
Advanced acceleration
Simulation
Backend flow (synthesis-only)
Backend flow (complete)
Session 1
Session 2
Session 3
[Apr-02/03]
Obj-1: mult2
Obj-2: mult3

## Slide 17: Data Hazard Resolution
# load operands ld x8, 0(x0) ld x9, 8(x0) ld x10, 16(x0) ld x11, 24(x0) ld x12, 32(x0) ld x13, 40(x0) ld x14, 48(x0) ld x15, 56(x0) ld x16, 64(x0) ld x17, 72(x0) # multiplication mul x18, x8, x9 mul x19, x10, x11 mul x20, x12, x13 mul x21, x14, x15 mul x22, x16, x17 #sums addi x23, x0, 0 nop nop nop add x23, x23, x18
nop
nop
nop
add x23, x23, x19
nop
nop
nop
add x23, x23, x20
nop
nop
nop
add x23, x23, x21
nop
nop
nop
add x23, x23, x22
nop
nop
nop
nop
MULT2
# load operands ld x8, 0(x0) ld x9, 8(x0) ld x10, 16(x0) ld x11, 24(x0) ld x12, 32(x0) ld x13, 40(x0) ld x14, 48(x0) ld x15, 56(x0) ld x16, 64(x0) ld x17, 72(x0)
# multiplication mul x18, x8,x9 mul x19, x10, x11 mul x20, x12, x13 mul x21, x14, x15 mul x22, x16, x17
#sums addi x23, x0, 0 add x23, x23, x18 add x23, x23, x19 add x23, x23, x20 add x23, x23, x21 add x23, x23, x22
MULT3
x23 dependency
Pipeline clean up
nop
nop
nop
nop
Data Hazard resolved!
Pipeline clean up is still required!
Software: Insert ‘nop’ to delay the pipeline.
Hardware: forwarding mechanism required.

## Slide 18: Data Hazard Example
Data is sent from the future.
Patterson Book. FIGURE 4.50

## Slide 19: Data Hazard Resolution: Hardware
Patterson Book. FIGURE 4.51
Forwarding from pipeline “shortcuts”

## Slide 20: Data Hazard Resolution – MULT3
Implement this MEM->EX forwarding at least.
Notes: rs1_ID_EX == rd_EX_MEM ?

## Slide 21: Implementation: Forwarding unit
// your_fw_fname.v or an/existing/Verilog/file
module YOUR_FW_UNIT_NAME#(
parameter integer … (if needed)
)(
input …,
input [ ?:0] …,
output [ ?:0] …
);
YOUR_FW_UNIT_LOGIC;
endmodule
Refer to slides: Implementation Method

## Slide 22: Obj-2: mult3
Pipelined processor with data hazard resolution
  Implement a forwarding unit to resolve the data hazard
  Run MULT3
  Run backend flow
    Synthesize
  Complete the report
MULT3
# load operands ld x8, 0(x0) ld x9, 8(x0) ld x10, 16(x0) ld x11, 24(x0) ld x12, 32(x0) ld x13, 40(x0) ld x14, 48(x0) ld x15, 56(x0) ld x16, 64(x0) ld x17, 72(x0)
# multiplication mul x18, x8,x9 mul x19, x10, x11 mul x20, x12, x13 mul x21, x14, x15 mul x22, x16, x17
#sums addi x23, x0, 0 add x23, x23, x18 add x23, x23, x19 add x23, x23, x20 add x23, x23, x21 add x23, x23, x22
Note:
Do not forget to update files_verilog.f in /SIM folder, if you add new RTL source file, or change the RTL location.
Please refer to the mux-2 to customize a mux-3, if needed.
Do not forget to add/modify all the signal wires in the top cpu.v according to your new modules.

## Slide 23
Today’s session: Backend flow
The RTL design is synthesized into a gate-level netlist.
Decide on the chip area and set memory macros location in the chip.
The synthesized gates are placed in the chip according to the floorplan.
A clock tree is generated to distribute the clock signal throughout the chip, while minimizing skew and ensuring timing requirements are met.
The global routing involves determining the overall routing paths between the blocks and macros; The detailed routing creates the actual metal interconnects between the gates.
Design rule checking: Once the routing is complete, the design is checked against a set of design rules to ensure that it is manufacturable.
Obj-1: mult2
Obj-2: mult3

## Slide 24: Today’s session: task summary
With session_guide.pdf
Study the RUN CYCLE-ACCURATE SIMULATION and RUN BACKEND FLOW
Follow the TASKS TO BE DONE and fill in the report.docx
Copy-paste your finished /RTL/*.v into the SOLUTION folders.
Obj-1  RTL_SOLUTION3_pipeline_basic_MULT2
Obj-2  RTL_SOLUTION4_pipeline_hazard_MULT3
Note:
We use universal test patterns for fair grading.
Do not modify cpu_tb.v & sky130_sram_2rw.v
Do not modify *mem_content.txt